YL-4000-H

Installation & Operation Manual

Attention

▲ For damage caused during the shipment, the buyer shall claim compensation to the carrier.

▲ Safety performance designed and manufactured to take into consideration. However, proper training and thorough handling can also increase safety. Do not operate or repair the lift before reading the instructions.

▲ Find out the power supply and current status and other requirements on the motor nameplate, there must be professional qualified electricians.

▲ In order to ensure life safety and avoid electric shock accidents, please ensure that all connection points are grounded.

▲ The company does not inform you of the local structural improvement of the product. No obligation for updates of previously sold products.

▲  Please read and fill out the last page of this manual, warranty card, and feedback to the dealer and the Company for the record. For providing one of the basis of after-sales service.Otherwise regarded as a waiver of the right to enjoy the same services at your own risk.

▲ Shall enhance more than the rated lift-off weight (4.0 tons) load.

▲ Reading devices on the warning signs carefully.

Table of Contents

1. Main Performance of the Lift............................................................................................................ 4

- Basic Parameters of the Lift............................................................................................................. 4

- Dimensions of the Lift.......................................................................................................................5

- Lift Installation.................................................................................................................................. 5

- Commissioning of the Lift................................................................................................................. 6

6. Maintenance and Inspection of the Lift.............................................................................................. 7

7. Parts Decomposition Diagram and Details of the Lift.........................................................................8

- Hydraulic System and Electrical Components of the Lift..................................................................35

9. Common Troubleshooting Method.............................................................................................................40

10. Box Packing List........................................................................................................................................41

11.Vulnerable Parts List............................................................................................................................42

- Main Performance of the Lift

● Set inspection, maintenance, parking function as one, beautiful appearance.

● Hydraulic cylinder drive, steel wire rope drive, quiet working environment.

● Mechanical safety lock, can be arbitrarily locked at the required height for operation, safe and reliable.

● The bridge plate can be adjusted horizontally in the locked position to meet the needs of accurate inspection, repair and parking.

● Install a special mobile pulley, the whole set of elevator can move freely by one person.

- Basic Parameters of the Lift

1. Max.lifting Weight: 4,000 kg

2. Maximum Lifting Height: 2,200 mm

3 Minimum Platform Height: 130 mm

- Runway Length: 4,200 mm

5. Runway Width: 475mm

6 Runway Inside Spacing: 955mm

7. Power Supply: Single-Phase, 240V / 50HZ 3HP (2.2 KW)

(Can be customized according to customer request)

- Dimensions of the Lift

Reference (Figure 1).

- Lift Installation

Step 1: Before installing the new lift, pay attention to the following matters:
1). The position of the lift should be considered according to the requirements of the design and planning plan of the whole field, and the placement size has enough space as far as possible.
2). According to the size of the foundation drawing in Figure 1, determine the installation position and draw the line.

3). Determine that the ground is free of any defects, and ensure that the strength of the foundation concrete reaches 3000psi(2.1kg/m m²)

4.) Open the box to check whether the missing pieces and transport damage. Required by the packing list.

Step 2: Install the column and beam (Z-1, Z-2), install the column cover plate, and drop the safety hook of the beam into the square hole of the safety plate.（Z-2,Z-2-1,Z-2-2）。

Step 3: Install the beam and runway, wire rope and cover.（Z -3,Z-3-1,Z-3-2,Z-3-3,Z-3-4）。

Step 4: Install the power unit and the oil pipe (Z-4).

Step 5: Install the manual unlock part (Z-5, Z-5-1, Z-5-2, Z-5-3, Z-5-4, Z-5-5).

Step 6: Install jack tray/tool box, rubber brake pad, plastic oil pan.（Z-6）(Optional Part)

Step 7: Install the mobile caster kit (Z-7). (Optional Part)

Step 8: Connect the power supply according to the requirements on the motor nameplate, and add the hydraulic oil.

Step 9: Point to move up, pay attention to observe whether the position of the wire rope is correct. Electromagnet unlock insurance down the runway to the lowest point, adjust the tension of the wire rope, make the four consistent.

Step 10: Adjust the position between the column component and the crossbeam. The limit block is required to be close to the column. Adjust the vertical of the column to the ground plane with the iron insert. Make the anchor bolt holes and the fastening bolts.

Step 11: Adjust the level of the runway. Raise a certain height to lock it up. Measure the level. When you need to adjust it, adjust the nut to the required position and lock it tightly.

Step 12: Check all labels and finishing.

- Commissioning of the Lift

☞ Fill the power unit tank with oil (hydraulic oil plate: N32 or N46).

☞ Move the rising start button to make the runway frame rise and remove the support frame. Pay special attention to the first point movement to observe whether the wire rope is pulling

In the wheel, take the correct position.

☞ Press the drop button to make the elevator in the normal drop lock, and observe whether the lock block can effectively enter the square hole of the lift bar.

☞ Lower the runway to the lowest position and adjust the nuts on the four steel ropes to make the same tension.

☞ No-load test run up and down twice to check whether each part works normally. Runway lock reliability check, repeat several times to check whether the hydraulic system works normally.

Special Attention

▲ Vehicles parked on the runway have to brake and use tire wedges.

▲ When lifting and lowering the vehicle, pay attention to the surrounding people and things to keep a distance can not be close to the elevator.

▲ The four columns should be perpendicular to the ground plane after installation, otherwise there will be danger in use!

▲ Before the drop operation must first move up a little, so that the lock block away from the square hole of the lifting bar, can drop. Otherwise, it will cause the damage to the control mechanism.

- Maintenance and Inspection of Lift

Daily Maintenance and Inspection

- Check the working position of the safety lock during the operation

- Check the unlocking and padlock of the safety lock and the column cover

- Check the hydraulic joint, air pipe joint and the hose for leakage

- Check the connection of the wire rope —— whether it is bent, broken and loose.

- Check the wear condition during the wire rope lifting process.

- Check all card spring connections and be reliable.

- Check the connection of all bolts, nuts and screws; —— If found loosening, tighten immediately

- Check the wires and switches for damage.

- Check the foundation strength around the expansion bolts.

- After the lift is operational, lubricate the cable shaft at least once a year or regularly

Weekly Maintenance and Inspection

- Check the strength and connection of the expansion bolts, and tighten them immediately

- Check the foundation strength around the expansion bolts

- Check the hydraulic oil level height

- Check and tighten the loose bolts, nuts, and screws

- Check the coordination of all wheel and wheel shaft

Monthly Maintenance and Inspection

- Lubricate the cable wheel and the cable wheel shaft

- Check the wear of the wire rope and replace it immediately with serious wear

- Replace hydraulic oil.

7. Parts Decomposition Diagram and Schedule of the Lift

Figure 1

1-2-5-22-23-25 （23-25  Optional Part）

3-4-8-9-10-11-12-14-15-16-21-24

6-7-12-19-20

17-18

26-27-28-29-30-31-32-33-34-35-36-37-47-48-49-50-51

38-39-40-41-42-43-44-45-46-52-53-54-55-56-57-58-59-70-99-100

60-64-73-74-78

61-62-65-66-67-68-69-71-72-75-76-77

79-80-81-82-87-88-90-91-92-93-94

83-84-85-86-98-104

95-96-97-103-105-107

101-102-106 （Optional Part)

ZPT-1

ZPT-1-1

ZPT-1-2

ZPT-1-3

ZPT-2

ZPT-2-1

ZPT-2-2

ZPT-3

ZPT-4 （Optional Part）

Z-1

Z-2

Z-2-1

Z-2-2

Z-3

Z-3-1

Z-3-2

Z-3-3

Z-3-4

Z-4

Z-5

Z-5-1

Z-5-2

Z-5-3

Z-5-4

Z-5-5

Z-6

Z-7

Z-8

Parts List

| Main Number | Sub Number | Product Name | Quantity / machine |
| --- | --- | --- | --- |
| PP8H 4-Column Lift Machine-Manual Edition |
| Welding Portion |
| 1 |  | Main column assembly | 1 |
| 2 |  | Sub-column assembly | 3 |
| 3 |  | Left assembly of the column cover plate | 2 |
| 4 |  | Right assembly of the column cover plate | 2 |
| 5 |  | Column cover sheet assembly | 4 |
| 6 |  | Main platform assembly | 1 |
| 7 |  | Sub-platform assembly | 3 |
| 8 |  | Oil cylinder growth rate wheel-axle assembly | 1 |
| 9 |  | Main Platform A-Single hole | 2 |
| 10 |  | Main platform B rope wheel shaft assembly-double holes | 2 |
| 11 |  | Linked assembly | 8 |
| 12 |  | The beam assembly | 2 |
| 13 |  | Left hand safe hook | 2 |
| 14 |  | The right hand moves the safe hook | 2 |
| 15 |  | Stop stop hook assembly | 4 |
| 16 |  | Cross-beam steel wire rope wheel shaft assembly | 4 |
| 17 |  | Left shield assembly | 2 |
| 18 |  | Right shield assembly | 2 |
| 19 |  | Insurance handle assembly | 1 |
| 20 |  | Safety rod assembly | 1 |
| 21 |  | Lrod connector assembly | 1 |
| 22 |  | Car board assembly | 4 |
| 23 |  | Mobile rack assembly | 4 |
| 24 |  | Mobile frame pin welding assembly | 4 |
| 25 |  | Tooldisc assembly | 2 |
| Standard Parts |
| 26 |  | M5X15 round-head bolt | 6 |
| 27 |  | M615 round-head bolt | 4 |
| 28 |  | M620 flat-head screw | 2 |
| 29 |  | M810 tightening bolts | 4 |
| 30 |  | M815 outer hexagon bolt | 12 |
| 31 |  | M8X20 flat-head bolt | 1 |
| 32 |  | M8X30 external hexagonal bolt | 4 |
| 33 |  | M835 outer hexagon bolt | 36 |
| 34 |  | M850 outer hexagon bolt | 4 |
| 35 |  | M1030 outer hexagon bolt | 16 |
| 36 |  | M1230 external hexagonal bolt | 16 |
| 37 |  | M18100 external hexagonal bolt | 16 |
| 38 |  | φ 5 flat pad | 6 |
| 39 |  | φ 6 flat pad | 6 |
| 40 |  | φ 8 flat pad | 56 |
| 41 |  | φ 10 flat pad | 32 |
| 42 |  | φ 12 flat pad | 32 |
| 43 |  | φ 14 flat pad | 1 |
| 44 |  | φ 18 flat pad | 48 |
| 45 |  | φ 20 flat pad | 20 |
| 46 |  | φ 25 flat pad | 24 |
| 47 |  | φ 6 pad | 6 |
| 48 |  | φ 8 pad | 52 |
| 49 |  | φ 10 Bullet | 16 |
| 50 |  | φ 12 Pack | 16 |
| 51 |  | φ 18 Bullet Pad | 16 |
| 52 |  | M5 nut | 6 |
| 53 |  | M6 nut | 2 |
| 54 |  | M8 nut | 14 |
| 55 |  | M8 self-locking nut | 16 |
| 56 |  | M10 nut | 16 |
| 57 |  | M12 nut | 18 |
| 58 |  | M18 nut | 32 |
| 59 |  | M20 nut | 8 |
| Column Assembly Part |
|  | 1 | Main column assembly | 1 |
|  | 2 | Sub-column assembly | 3 |
| 60 |  | power unit | 1 |
| 61 |  | 9 / 16 tip power unit connector | 1 |
| 62 |  | ￠ 14 Copper seal gasket | 1 |
|  | 33 | M835 outer hexagon bolt | 4 |
|  | 40 | φ 8 flat pad | 8 |
|  | 48 | φ 8 pad | 4 |
|  | 54 | M8 nut | 4 |
|  | 3 | Left assembly of the column cover plate | 2 |
|  | 4 | Right assembly of the column cover plate | 2 |
|  | 36 | M1230 external hexagonal bolt | 16 |
|  | 42 | φ 12 flat pad | 32 |
|  | 50 | φ 12 Pack | 16 |
|  | 57 | M12 nut | 16 |
|  | 5 | Column cover sheet assembly | 4 |
|  | 44 | φ 18 flat pad | 16 |
|  | 58 | M18 nut | 16 |
| 63 |  | Foot al bracket (option) | 1 |
| Platform Assembly part |
|  | 6 | Main platform assembly | 1 |
|  | 7 | Sub-platform assembly | 3 |
| 64 |  | hydro-cylinder | 1 |
| 65 |  | General use for the cylinder tail shaft SH | 1 |
| 66 |  | φ 35 card spring | 2 |
| 67 |  | Oil cylinder slider bracket | 1 |
|  | 30 | M815 outer hexagon bolt | 2 |
|  | 48 | φ 8 pad | 2 |
|  | 40 | φ 8 flat pad | 2 |
| 68 |  | Oil cylinder slider | 2 |
|  | 28 | M620 flat-head screw | 2 |
|  | 39 | φ 6 flat pad | 2 |
|  | 47 | φ 6 pad | 2 |
|  | 53 | M6 nut | 2 |
| 69 |  | Growth wheel | 4 |
|  | 8 | Oil cylinder growth rate wheel-axle assembly | 1 |
| 70 |  | M10 butter mouth | 1 |
|  | 31 | M8X20 flat-head bolt | 1 |
| 71 |  | A 90-degree ZG 3 / 8 internal and external connector | 1 |
| 72 |  | 9 / 16 The tip | 1 |
| 73 |  | Double-head 9 / 16 pointed tubing is always bent | 1 |
| 74 |  | Double straight 9 / 16 tip live catch oil tubing | 1 |
| 75 |  | Right-angle elbow 9 / 16 tip | 1 |
|  | 43 | φ 14 flat pad | 1 |
| 76 |  | Bend nut | 1 |
| 77 |  | 1 / 4 return oil pipe direct head | 1 |
| 78 |  | air tube | 1 |
| 79 |  | wire rope pulley | 6 |
|  | 46 | φ 25 flat pad | 12 |
| 80 |  | 1-inch galvanized tube 18 | 2 |
| 81 |  | 1-inch galvanized tube 44 | 2 |
|  | 9 | Main Platform A-Single hole | 2 |
|  | 10 | Main platform B rope wheel shaft assembly-double holes | 2 |
|  | 70 | M10 butter mouth | 4 |
| 82 |  | Main platform wire rope lock plate | 1 |
|  | 30 | M815 outer hexagon bolt | 6 |
|  | 40 | φ 8 flat pad | 6 |
|  | 48 | φ 8 pad | 6 |
| 83 |  | 9.53, L1=6185 | 1 |
| 84 |  | 9.53, L2=7610 | 1 |
| 85 |  | 9.53, L3=10250 | 1 |
| 86 |  | 9.53, L4=11690 | 1 |
|  | 59 | M20 nut | 8 |
|  | 45 | φ 20 flat pad | 8 |
|  | 11 | Linked assembly | 8 |
|  | 37 | M18100 external hexagonal bolt | 16 |
|  | 44 | φ 18 flat pad | 32 |
|  | 51 | φ 18 Bullet Pad | 16 |
|  | 58 | M18 nut | 16 |
| The beam assembly part |
|  | 12 | The beam assembly | 2 |
|  | 13 | Left hand safe hook | 2 |
|  | 14 | The right hand moves the safe hook | 2 |
|  | 55 | M8 self-locking nut | 4 |
| 87 |  | Bound axle | 4 |
|  | 45 | φ 20 flat pad | 12 |
|  | 15 | Stop stop hook assembly | 4 |
| 88 |  | Stop fall hook limit wheel pin | 4 |
| 89 |  | Stop fall hook limit wheel | 4 |
|  | 40 | φ 8 flat pad | 4 |
|  | 48 | φ 8 pad | 4 |
|  | 55 | M8 self-locking nut | 4 |
| 90 |  | Twist spring-left | 2 |
| 91 |  | Twist spring-right | 2 |
| 92 |  | A 6-minute galvanized pipe 17 | 4 |
| 93 |  | Pull spring (￠ 1.6 ￠ 12 72) | 8 |
|  | 16 | Cross-beam steel wire rope wheel shaft assembly | 4 |
|  | 30 | M815 outer hexagon bolt | 4 |
|  | 40 | φ 8 flat pad | 4 |
|  | 48 | φ 8 pad | 4 |
|  | 46 | φ 25 flat pad | 12 |
|  | 78 | wire rope pulley | 4 |
| 94 |  | The beam rope wheel is separated | 4 |
|  | 29 | M810 tightening bolts | 4 |
|  | 70 | M10 butter mouth | 4 |
|  | 34 | M850 outer hexagon bolt | 4 |
| 95 |  | The beam slider | 8 |
|  | 33 | M835 outer hexagon bolt | 32 |
|  | 40 | φ 8 flat pad | 32 |
|  | 48 | φ 8 pad | 32 |
|  | 17 | Left shield assembly | 2 |
|  | 18 | Right shield assembly | 2 |
|  | 27 | M615 round-head bolt | 4 |
|  | 39 | φ 6 flat pad | 4 |
|  | 47 | φ 6 pad | 4 |
| The whole machine assembly part |
|  | 19 | Insurance handle assembly | 1 |
|  | 20 | Safety rod assembly | 1 |
|  | 21 | Lrod connector assembly | 1 |
|  | 57 | M12 nut | 2 |
| 96 |  | The safety rod is separated | 2 |
| 97 |  | Beam Unlock bar A-220 | 2 |
| 98 |  | Beam unlock lever B-2160 | 2 |
| 99 |  | M8 fish eye bearing | 8 |
| 100 |  | M8 ring bolt | 4 |
|  | 32 | M8X30 external hexagonal bolt | 4 |
|  | 54 | M8 nut | 10 |
|  | 55 | M8 self-locking nut | 8 |
|  | 22 | Car board assembly | 4 |
| 101 |  | Nylon slider | 4 |
|  | 26 | M5X15 round-head bolt | 6 |
|  | 38 | φ 5 flat pad | 6 |
|  | 52 | M5 nut | 6 |
| 102 |  | Fighter board | 4 |
| 103 |  | Rubber brake adhesive pad | 2 |
|  | 25 | Tooldisc assembly | 1 |
| 104 |  | Plastic drip oil pan | 4 |
|  | 23 | Mobile rack assembly | 4 |
|  | 24 | Mobile frame pin welding assembly | 4 |
| 105 |  | Type R elastic pin | 4 |
| 106 |  | φ 150 | 4 |
|  | 35 | M1030 outer hexagon bolt | 16 |
|  | 41 | φ 10 flat pad | 32 |
|  | 49 | φ 10 Bullet | 16 |
|  | 56 | M10 nut | 16 |
| 107 |  | film | 8 |

8. Hydraulic System and Electrical Components of the Lift

- External explosion diagram of the hydraulic station

- Hydraulic system of the elevator

a. Hydraulic schematic diagram

b. Schedule of hydraulic components

c. Operating principle of the hydraulic system

d. Electrical schematic diagram

1. Appearance and Explosion Diagram of the Hydraulic Station

| Order No. | Name | Qty. | Order No. | Name | Qty. |
| --- | --- | --- | --- | --- | --- |
| A1 | electric motor | 1 | A9 | gland | 1 |
| A2 | spool | 1 | A10 | bulkhead | 1 |
| A3 | fuel tank | 1 | A11 | M5X40 external hexagon screw | 4 |
| A4 | Drop the speed regulating valve | 1 | A12 | Φ 5 flat pad | 4 |
| A5 | bulkhead | 1 | A13 | Φ 5 pad | 4 |
| A6 | oil-out | 1 | A14 | M6X20 external hexagon screw | 4 |
| A7 | oil-out | 1 | A15 | Φ 6 flat pad | 4 |
| A8 | Hand pull valve | 1 | A16 | Φ 6 pad | 4 |

2.  The Hydraulic System

A. Hydraulic Schematic Diagram

B. Schedule of Hydraulic Components

| A9 | hydro-cylinder |  |  | 1 |  |
| --- | --- | --- | --- | --- | --- |
| A8 | hand valve |  |  | 1 |  |
| A7 | check valve |  |  | 1 |  |
| A6 | Drop throttle valve |  |  | 1 |  |
| A5 | oil pump |  |  | 1 |  |
| A4 | overflow valve |  |  | 1 |  |
| A3 | fuel tank |  |  | 1 | Volume 10 litres |
| A2 | oil filter |  |  | 1 |  |
| A1 | any power-generating or power-driven machine |  |  | 1 |  |
| Order No. | Name | Model | Specifications | Number of packages | Remarks |

C. The working principle of the hydraulic system is as follows:

When the start button on the hydraulic station is pressed, the motor starts to drive the oil pump and takes the pressure oil from the tank to the No. A9 cylinder to move the piston rod. At this time, the A4 overflow valve is closed, and the pressure is adjusted before leaving the factory. Ensure the rated load requirements of the lifting. However, when the pressure in the system exceeds the limit, the automatic overflow valve discharges the oil. Release the start button, stop the oil supply, finish the lifting, and start the operation. If it drops, first move up a little, pull open the mechanical safety lock, press the manual valve A8 to start unloading the oil drop.

D Electrical Schematics (240V single-phase generator or according to customer requirements)

(During installation, the wiring must be conducted according to the schematic diagram to ensure that each connection is grounded reliably, and the input power supply must be equipped with leakage and overcurrent protection switches)

| SB | Point motion press twist | LXW5-11M/L | 1 |
| --- | --- | --- | --- |
| KM | AC contactor | CJX1-6.3/01-240V | 1 |
| Code Name | Name | Model | Quantity |

9. Common Troubleshooting Method

| Order No. | Fault Phenomenon | The Exclusion Method |
| --- | --- | --- |
| 1 | The motor does not turn | ● Check whether the power supply is electric ● Check whether the wiring in the motor junction box is loose |
| 2 | Motor rotation without pressure oil | ● The single-phase electric rotation direction is wrong, and the position of two of the incoming lines is changed. ● Check whether the suction pipe in the oil tank falls off. |
| 3 | The hydraulic pressure drops slowly after lifting (Poor pressure) | ● Clean the check valve and the reversing valve of the power unit. |
| 4 | The safety lock can't be locked | Observe whether the position of the lock safety hook is normal. Observe whether the column is positioned correctly. Check the reset spring action of the safety hook. |
| 5 | Motor and electrical appliances failure | ● Cut off the power supply in time, check, repair and replace by a professional electrician. |
| 6 | Else | ● Other found work is not normal, can be telephone consultation. Willing to provide services for you. |

10. Box Packing List

|  |  | Boating parts |  |
| --- | --- | --- | --- |
| Installation site | Order number | Product name | Quantity / machine |
| power unit | 33 | M835 outer hexagon bolt | 4 |
| power unit | 40 | φ 8 flat pad | 8 |
| power unit | 48 | φ 8 pad | 4 |
| power unit | 54 | M8 nut | 4 |
| Column cover plate | 36 | M1230 external hexagonal bolt | 16 |
| Column cover plate | 42 | φ 12 flat pad | 32 |
| Column cover plate | 50 | φ 12 Pack | 16 |
| Column cover plate | 57 | M12 nut | 16 |
| power unit | 61 | 9 / 16 tip power unit connector | 1 |
| power unit | 62 | ￠ 14 Copper seal gasket | 1 |
| power unit | 73 | Double-head 9 / 16 pointed tubing is always bent | 1 |
| fixed platform | 37 | M18100 external hexagonal bolt | 16 |
| fixed platform | 44 | φ 18 flat pad | 32 |
| fixed platform | 51 | φ 18 Bullet Pad | 16 |
| fixed platform | 58 | M18 nut | 16 |
| terrace | 103 | Rubber brake adhesive pad | 2 |
| parts and components | 70 | M10 butter mouth | 9 |
| parts and components | 97 | Beam Unlock bar A-220 | 2 |

- Vulnerable Parts List

|  |  | quick-wear part |  |
| --- | --- | --- | --- |
| Installation site | order number | product name | Quantity / machine |
| hydro-cylinder | 68 | Oil cylinder slider | 2 |
| hydro-cylinder | 69 | Growth wheel | 4 |
| Platform beam | 79 | wire rope pulley | 6 |
| terrace | 83 | 9.53, L1=6185 | 1 |
| terrace | 84 | 9.53, L2=7610 | 1 |
| terrace | 85 | 9.53, L3=10250 | 1 |
| terrace | 86 | 9.53, L4=11690 | 1 |
| crossbeam | 95 | The beam slider | 8 |
| Get on the board | 101 | Nylon slider | 4 |
| parts and components | 103 | Rubber brake adhesive pad | 2 |
| parts and components | 104 | Plastic drip oil pan | 4 |
| Mobile frame | 106 | φ 150 | 4 |
| Mobile frame | 107 | film | 8 |