YL-5500

5.5Ton Four post car hoist Installation & Operation Manual

Special Note

▲ Shipping process caused damage to the equipment by the purchaser claims to the carrier unit.

▲ Design and manufacturing, taking into account the safety performance. However, proper training and careful operation can also increase security. Not reading the manual, shall not operator repair the device.

▲ To identify the requirements of the motor nameplate power, current status, must be professionally qualified electrician electrical connection.

▲ To ensure that the life safety and to avoid electric shock accident occurred, to ensure reliable grounding of all ground.

▲ The anger of the local structure of the product improvement without notice. Under no obligation to update on previous sales of the product.

▲ Please read and fill out the last page of this manual, warranty card, and feedback to the dealer and the Company for the record. For providing one of the basis of after-sales service.Otherwise regarded as a waiver of the right to enjoy the same services at your own risk.

▲ Shall enhance more than the rated lift-off weight (5.5 tons) load.

▲ Reading devices on the warning signs carefully.

Table of Contents

1. Equipment performance

2. The basic parameters

3. Equipment Dimensions

4. The installation of equipment

5. Equipment debugging

- Equipment maintenance and inspection

7.Pneumatic insurance installation and instruction

8. Parts of the device exploded view and schedule

9. Hydraulic system equipment and electrical component

10. Common troubleshooting method

- Packing list

- Wearing part list

Equipment performance

● Set inspection, maintenance, four positioning as a whole, and beautiful appearance.

● Hydraulic cylinders drive, rope drive, quiet working environment.

● Mechanical safety lock, can any of the top job at the desired height, safe and reliable.

● The levelness of concrete slab in the locked position can be adjusted to meet the needs of the precise wheel alignment.

● Common type designed for the inspection and repair purposes.

● Wheel alignment special. Additional two sets of sliding panels and a secondary lifting.

Basic parameters of the equipment

1.  A rated lifting weight:   5.5 tons

- Lifting height:         1850 mm

- Min height:           241 mm

4.  Runway Length:       5160 mm

5. The runway width:       508 mm

6. Runway Inside distance:  1078 mm

7.  Power supply:         240V/50HZ  (3KW)

The device dimensions of machine

Check the FIG 1

The installation of equipment

The first step: site selection

Before installing the new lift, pay attention to the following matters:

(1) The location of the lift, according to the design and planning of the entire plan requirements, as far as possible, place the dimension there is sufficient space.

(2) According Figure 1 foundation size , determine the installation location and carry out the dash.

(3) Make sure the ground does not have any defects to ensure that the basis of concrete strength of 3000psi (2.1kg/mm ²)

- Open the box to check whether the missing pieces and transport damage. Required by the packing list.

Step 2: Connect the runway and the beam (Figure 2)

Step 3: Install the four column parts (Figure 2)

Step 4: Install the power unit and pipeline joints(Figure 2) (Figure 5)

Step 5: Install a safety lock device (Figure 3) (Figure 6) (Figure 8)

Step 6: The need to do a wheel alignment equipment, installation,sliding, corner plate (user optional) and the second lifting

Step 7: The power supply according to the requirements on the motor nameplate, add hydraulic oil.

Step 8: Jog up, observe the correct rope position (Figure 7) (Figure 8) . Relieve the support under the runway to runway decreased to the lowest point, adjusting the tension of the wire rope, the four unanimously.

Step 9: Adjust the position between the column components and beams (Figure 2) . Requirements limit block close to the column side. Iron inserts to adjust the vertical column and the ground plane. Drilling bolt hole and tighten the bolt.

Step 10: Adjust the levelness of the runway (Figure 2) (Figure 8). Ascending to a height. Lock levelness, When need to adjust. Adjust nut（11）to the required position. Then lock.

Step 11: Install all shrouding  (Figure 2) .

Step 12: Install running board and slopes (Figure 2)

Step 13: Stick all labels and finishing.

The debugging

☞ Hydraulic station to fill the tank pressurized oil N32 or N46

☞ To move the start button, so that the runway frame rise, removal of the support frame. Special attention to the first jog observe whether rope in the embrace of a round tank, location to be correct.

☞ Pull the handle pressure in the unlocking state to observe the lock block ability to effectively disengage the insurance piece square hole, if necessary, adjust the lift rod length (Figure 3，6，8 ).

☞ Down the runway rack to lowest position, adjust the nuts on the four wire rope, so that tension is the same. (Figure 2.8).

☞ Adjust the level of the runway: press the start button, the runway frame up by the appropriate location, drop the runway according to decline in valve on the hydraulic station. Matter of four lock set limit Article hole. Level detection level of the runway,to be adjusted with reference to the installation Step 10.

☞ No-load test up and down twice, check each part is working properly. Runway lock reliability checks, and more repeated several times re-planted on the car to check the hydraulic system is working properly.

Special attention

▲ Vehicles parked on the runway braking and tire wedge.

▲ Lifting and lowering vehicles, pay attention to people and things around to keep their distance and not close to the lift.

▲ Maintenance man to enter the work area, check the runway should be properly locked in the column lift.

▲ Four column installation should be vertical to the ground plane, otherwise be dangerous to use!

▲ Decline before the operation must be the first point of action to rise a little, so that the lock block to leave the lift bar square hole in order to decline. Otherwise it will cause damage to the control mechanism

Maintenance and inspection notes

Routine maintenance and inspection

- Check work location of safety lock when operation

2. Check safety lock and unlock the insurance piece and padlock

3. Check hydraulic fittings, hose leaks

4. Check the wire rope connections - is bent, broken, loose.

5. Check the wear of the wire rope lifting process.

6. Check all retainer connection must be reliable connection.

7. Check all bolts, nuts, screws connection - found loose shall immediately tighten

8. Check wires and switches for damage.

9. Check expansion bolts around the foundation strength.

10.After the lift is put into use, oil refers to the gun at least once a year or at regular intervals on the cable axle lubrication

Weekly maintenance and inspection

1. Check the bolts strength and connections found loose shall immediately tighten

2. Inspection inflation bolt around the foundation strength

3. Check the hydraulic oil liquid level

4. Check and tighten loose bolts, nuts, screws

5. Check all pulley and pulley axle

Monthly maintenance and inspection

1. Lubricate the cable wheel and cable axle

2. Check the wire rope wear, severe wear and tear be replaced immediately

3. Replace the hydraulic oil.

Pneumatic insurance installation and instruction

- Installation

Installation oil-mist separator(124) (Figure 2，6),installation hand valve（129）（Figure 6),Then press the up button to the required height, connect air pipe 128,130,132. ,Then pull our the nut which on oil-mist separator, adjust the pressure to 0.6MPA-0.8MPA，then press the nut back.

2.Instruction

- Rising the lift to the required height, press the down handle A8 ( Power unit drawing), the devices locking, convenience for work.

- After maintain, Point press the up button, it will raise a little, then release the hand valve (129) (Figure 6), then press the down handle A8，the lift will down to the lowest position.

Parts of the device exploded view and schedule

Figure 1

Figure 2

Figure 3

Figure 4

Figure 5

Figure 6

Figure 7

Figure 8

Lift part list

| No. | Name | Qty | Remark |
| --- | --- | --- | --- |
|  | Main Platform | 1 |  |
|  | Subsidiary Platform | 1 |  |
|  | Main column | 1 |  |
|  | Subsidiary column | 3 |  |
|  | Beam welding assembly | Each 1 | Bilateral symmetry |
|  | Hexagon bolt M12*30 | 20 |  |
|  | Flat gasket12 | 36 |  |
|  | Spring washer 12 | 20 |  |
|  | Nut M12 | 16 |  |
|  | Column top cover welding assembly | Each 2 | Bilateral symmetry |
|  | Nut M18 | 8 |  |
|  | Flat gasket 18 | 8 |  |
|  | Insurance piece | 4 |  |
|  | Stop running plate | 2 |  |
|  | Hexagon bolt M12*40 | 16 |  |
|  | Spring washer 12 | 16 |  |
|  | Flat gasket 12 | 16 |  |
|  | Locating plate welding assembly | 2 |  |
|  | Active plate 3 | 4 |  |
|  | Active plate 2 | 2 |  |
|  | Active plate 1 | 2 |  |
|  | Location plate of slide plate | 2 |  |
|  | Slide plate wheel frame welding assembly | 2 |  |
|  | Universal ball | 88 |  |
|  | Self-locking nut 12 | 4 |  |
|  | Flat gasket inner12 outsider 40 | 4 |  |
|  | Tension spring | 8 |  |
|  | Slide plate welding assembly | 2 |  |
|  | Key ring | 8 |  |
|  | Chain | 4 |  |
|  | Small up ramp assembly | 2 |  |
|  | hexagon socket bolt M12*35 | 4 |  |
|  | Flat gasket 12 | 28 |  |
|  | Spring washer 12 | 24 |  |
|  | Nut 12 | 24 |  |
|  | Big up ramp welding assembly | 2 |  |
|  | Up ramp protector | 2 |  |
|  | Screw M5*16 | 6 |  |
|  | Gasket 5 | 6 |  |
|  | Nut 5 | 6 |  |
|  | Up ramp axle | 2 |  |
|  | R type pin | 4 |  |
|  | Power unit | 1 |  |
|  | Brake block | 2 |  |
|  | Slide plate pin | 4 |  |
|  | Oil-mist separator protector | 1 |  |
|  | Beam welding assembly | Each 1 | Bilateral symmetry |
|  | Long beam side plate | 2 |  |
|  | Short beam side plate | 4 |  |
|  | Middle beam side plate | 2 |  |
|  | Beam head cover | 4 |  |
|  | Cup head screw M6*15 | 32 |  |
|  | Spring washer 6 | 36 |  |
|  | Flat gasket 6 | 36 |  |
|  | pulley limit pin | 4 |  |
|  | 12 Snap spring | 8 |  |
|  | Screw M6*25 | 8 |  |
|  | Nylon cushion | 8 |  |
|  | Self-lock nutM6 | 16 |  |
|  | Slide plate | 8 |  |
|  | Screw M8*20 | 24 |  |
|  | Screw M6*15 | 16 |  |
|  | Safety axle dam-board | 8 |  |
|  | Beam safety check ring | 4 |  |
|  | Beam safety axle | 4 |  |
|  | Air safety hook | Each 2 | Bilateral symmetry |
|  | Breakage insurance hook | 4 |  |
|  | Safety limit wheel | 4 |  |
|  | Beam safety limit axle | 4 |  |
|  | Hexagon bolt M6*25 | 8 |  |
|  | Black tension spring | 8 |  |
|  | Air cylinder assembly | 4 |  |
|  | Nipple | 4 |  |
|  | Hexagon bolt M8*15 | 4 |  |
|  | Spring washer 8 | 4 |  |
|  | Flat gasket 8 | 4 |  |
|  | Beam pulley axle welding assembly | 4 |  |
|  | Beam pulley check ring | 4 |  |
|  | Beam pulley | 4 |  |
|  | Flat gasket 40 | 8 |  |
|  | Main plate welding assembly | 1 |  |
|  | Hexagon bolt M8*15 | 2 |  |
|  | Spring washer 8 | 2 |  |
|  | Flat gasket 8 | 2 |  |
|  | Nipple | 2 |  |
|  | Platform pulley axle 1 | 1 |  |
|  | Beam pulley axle sleeve1 | 1 |  |
|  | Gasket 42 | 4 |  |
|  | Pulley 248 | 6 |  |
|  | Beam pulley axle 2 | 1 |  |
|  | Beam pulley axle sleeve2 | 1 |  |
|  | Beam pulley axle sleeve3 | 1 |  |
|  | Hexagon socket screw M10*20 | 1 |  |
|  | Flat gasket 10 | 3 |  |
|  | Spring washer 10 | 3 |  |
|  | Hexagon socket screwM10*40 | 2 |  |
|  | Main platform | 1 |  |
|  | Power unit | 1 |  |
|  | Hexagon bolt M8*25 | 4 |  |
|  | Flat gasket 8 | 8 |  |
|  | Hexagon bolt M12*40 | 2 |  |
|  | Spring washer 8 | 4 |  |
|  | Nut 8 | 4 |  |
|  | Copper backing | 1 |  |
|  | Through joint | 1 |  |
|  | Oil tube L=2340mm | 1 |  |
|  | American system 9/16 Nut | 1 |  |
|  | Flat gasket 14 | 1 |  |
|  | Big right angle bending | 1 |  |
|  | Oil tube L=2020mm | 1 |  |
|  | Explosion-proof valve assembly | 1 |  |
|  | Small angle bending | 1 |  |
|  | Oil cylinder | 1 |  |
|  | Silencer | 1 |  |
|  | wire rope pull plate | 1 |  |
|  | Slide block of cylinder pull plate | 2 |  |
|  | Screw M6*12 | 2 |  |
|  | wire rope lock plate | 1 |  |
|  | Self-lock nut30 | 1 |  |
|  | Oil cylinder limit base | 1 |  |
|  | Flat gasket 12 | 2 |  |
|  | Spring washer 12 | 2 |  |
|  | Nut 12 | 2 |  |
|  | Big oil-mist separator | 1 |  |
|  | Screw M6*15 | 4 |  |
|  | Spring washer 6 | 4 |  |
|  | Flat gasket 6 | 4 |  |
|  | L=800mm | 1 |  |
|  | Hand valve assembly | 1 |  |
|  | Air pipe L=2600mm | 1 |  |
|  | Tracheal tee | 3 |  |
|  | Air pipe 1 | 2 |  |
|  | Air pipe 2 | 1 |  |
|  | Tracheal pass-through | 1 |  |
|  | Air pipe 3 | 2 |  |
|  | Air pipe 4 | 2 |  |
|  | Air cylinder assembly | 4 |  |
|  | Pneumatic insurance hook | Each 2 | Bilateral symmetry |
|  | Nut 20 | 8 |  |
|  | Flat gasket 20 | 8 |  |
|  | Wire rope L=10703mm | 1 |  |
|  | Wire rope L=9126mm | 1 |  |
|  | Wire rope L=3966mm | 1 |  |
|  | Wire rope L=5543mm | 1 |  |
|  | Beam pulley | 4 |  |
|  | Runway pulley | 6 |  |

HYDRAULIC SYSTEM, ELECTRIC COMPONENT

AND WIRING DIAGRAM

1.Power unit out-looking explosion figure

2.Hydraulic system of equipment

a.Hydraulic schematic diagram

b.Hydraulic components list

c.Hydraulic system working principle

d.Electric schematic diagram

Power unit out-looking explosion figure

| No. | Name. | Qty | No. | Name | Qty |
| --- | --- | --- | --- | --- | --- |
| A1 | Motor | 1 | A9 | Sheet gasket | 1 |
| A2 | valve element | 1 | A10 | Choke plug | 1 |
| A3 | Tank | 1 | A11 | M5X40 hexagon screw | 4 |
| A4 | Down-regulating valve | 1 | A12 | Φ5 Flat gasket | 4 |
| A5 | Choke plug | 1 | A13 | Φ5 Spring washer | 4 |
| A6 | Oil-out | 1 | A14 | M6X20 hexagon screw | 4 |
| A7 | Oil-out | 1 | A15 | Φ6 Flat gasket | 4 |
| A8 | Hand valve | 1 | A16 | Φ6 Spring washer | 4 |

2．Hydraulic system

a．Hydraulic principle

b．Parts list

| A11 | Ball valve |  |  | 1 | Special purpose for jack beam (optional) |
| --- | --- | --- | --- | --- | --- |
| A10 | Cylinder |  |  | 1 | Jack beam oil cylinder (optional) |
| A9 | Cylinder |  |  | 1 |  |
| A8 | Hand valve |  |  | 1 |  |
| A7 | One-way valve |  |  | 1 |  |
| A6 | Throttle valve |  |  | 1 |  |
| A5 | Oil pump |  |  | 1 |  |
| A4 | Flood valve |  |  | 1 |  |
| A3 | Tank |  |  | 1 |  |
| A2 | Filter |  |  | 1 |  |
| A1 | Motor |  |  | 1 |  |
| No. | Name | Model | Standard | Qty | Remark |

c. The hydraulic system works as follows:

When pressing the start button on the hydraulic station , the motor starter to drive the pump suction pressure from the tank and oil is carried into the serial A9 fuel tank, so that the piston rod to move. The A4 relief valve closed, the pressure is fine before leave factory . To ensure that the requirements of lifting rated load. However, the system pressure exceeds the limit, automatic relief valve unloading. Release the start button, stop oil supply to enhance the end, began operations work. If you decline, the first point of action to rise a little, after the mechanical safety lock is opened, pressing the manual valve A8 and began unloading decreased.

Electrical schematic diagram (three-phase motor) (single-phase optional)

(* Installation sure to follow the schematic wiring to ensure reliable the ground at the ground, the input power leakage, over-current protection switch must be set)

| SB | button | LXW5-11M/L | 1 |
| --- | --- | --- | --- |
| KM | exchange contractor | CJX1-6.3/01-240V | 1 |
| No. | Name | Model | Qty |

Trouble shooting

| No. | Symptom | Eliminating methods |
| --- | --- | --- |
| 1 | A motor does not turn | ● check the power supply has power ● Check the motor connection box wiring is loose |
| 2 | motor rotation position of pressure oil | ● Three-phase electric rotating in the wrong direction, swap in which two into line. ● Check that the fuel tank suction tube is off |
| 3 | Hydraulic lift after the slow decline in(Pressure bad) | ● cleaning one-way valve and valve of the hydraulic station. |
| 4 | Security lock laughs at locksmith | ● observe the position of locksmith security hook plate is normal. ● observed the location of column is correct. ● Check the return spring safety hook plate |
| 5 | Motors, electrical failure | ● Promptly cut off the power to inspect, repair and replacement by a professional electrician.. |
| 6 | A motor does not turn | ● check the power supply has power ● Check the motor connection box wiring is loose |

Standard part packing list

| No. | Part name | Name | Qty | Remark |
| --- | --- | --- | --- | --- |
| 1 | Standard part | 18 Foundation bolt | 16 | With nut/ flat gasket/spring washer |
|  |  | Hexagon bolt M8Ｘ25 | 4 | With nut/ double flat gasket/spring washer |
|  |  | 12×30 screw | 20 |  |
|  |  | Round flat nose pad | 20 |  |
|  |  | Tie | 10 |  |
|  |  | M14Ｘ1.5-M16Ｘ1.5 | 1 | Joint of power unit |
|  |  | Ø14copper backing | 2 | Joint Sealing element |
|  |  | “0”type sealing element | 1 |  |
|  |  | Screw M8Ｘ20 | 24 | Slide block connect with beam |
|  |  | 8-2600 Air pipe | 1 | Main insurance |
|  |  | 8-800 Air pipe | 1 | Oil-mist separator to hand valve |
|  |  | Oil-mist separator | 1 |  |
|  |  | Hand valve | 1 |  |
|  |  | oil tube | 1 | L=2340 With protector |
|  |  | Screw M6Ｘ15 | 4 | Oil-mist separator with nut, flat gasket, spring washer |
|  |  | 12X40 Screw | 16 |  |
|  |  | Brake block | 2 |  |
|  |  | Nipple | 6 | axle of pulley |
|  |  | 12 Flat gasket | 52 |  |
|  |  | 12 Nut | 16 |  |
|  |  | 12 Spring washer | 36 |  |
|  |  | 8 Flat gasket | 8 |  |
|  |  | 8 Spring washer | 4 |  |
|  |  | 8 Nut | 4 |  |
|  |  | 6 Flat gasket | 4 |  |
|  |  | 6 Spring washer | 4 |  |

Wearing parts list

| No. | Model | Name |
| --- | --- | --- |
| 79 | 40-178 | Beam pulley |
| 146 | 40-248 | Platform pulley |
| 60 |  | slide block |
| 68 |  | Beam limit wheel |
| 137 | LMSAL16*45 | Air cylinder |
| 141 | L=10703-13 | Wire rope |
| 142 | L=9126-13 | Wire rope |
| 144 | L=5543-13 | Wire rope |
| 143 | L=3966-13 | Wire rope |
| 129 |  | Hand valve |
| 124 |  | Oil-mist separator |
| 44 |  | Brake block |